## Slide 1: Smart Garden

## Slide 2
Hardware: MCU
CC1310

## Slide 3
Hardware: MCU
CC1310 Launchpad
Feature:
MCU 32bit ARM Cortex-M3 processor 48MHz
Ultra low power
Sub 1Ghz RF devices
30 pins GPIO
Four General-Purpose Timer Modules
12-Bit ADC, 200 ksamples/s, 8-Channel Analog MUX
UART
2× SSI (SPI, MICROWIRE, TI)
I2C
SmartRF
Suitable for Systems Targeting Compliance With Worldwide Radio Frequency Regulations
  ETSI EN 300 220, EN 303 131, EN 303 204 (Europe)
  FCC CFR47 Part 15 (US)
  ARIB STD-T108 (Japan)
Wireless M-Bus and IEEE 802.15.4g PHY
IAR Embedded Workbench® for ARM
Notes: Microcontroller
  Powerful ARM® Cortex®-M3
  EEMBC CoreMark® Score: 142
  EEMBC ULPBench™ Score: 158
  Up to 48-MHz Clock Speed
  128KB of In-System Programmable Flash
  8KB of SRAM for Cache (or as General- Purpose RAM)
  20KB of Ultralow Leakage SRAM
  2-Pin cJTAG and JTAG Debugging
  Supports Over-the-Air Upgrade (OTA)
Ultralow Power Sensor Controller
  Can Run Autonomous From the Rest of the System
  16-Bit Architecture
  2KB of Ultralow Leakage SRAM for Code and Data
Efficient Code-Size Architecture, Placing TI-RTOS, Drivers and Bootloader in ROM
RoHS-Compliant Package
  7-mm × 7-mm RGZ VQFN48 (30 GPIOs)
  5-mm × 5-mm RHB VQFN48 (15 GPIOs)
  4-mm × 4-mm RSM VQFN48 (10 GPIOs)
Peripherals
  All Digital Peripheral Pins Can Be Routed to Any GPIO
  Four General-Purpose Timer Modules (Eight 16-Bit or Four 32-Bit Timers, PWM Each)
  12-Bit ADC, 200 ksamples/s, 8-Channel Analog MUX
  Continuous Time Comparator
  Ultralow Power Clocked Comparator
  Programmable Current Source
  UART
  2× SSI (SPI, MICROWIRE, TI)
  I2C
  I2S
  Real-Time Clock (RTC)
  AES-128 Security Module
  True Random Number Generator (TRNG)
  Support for Eight Capacitive Sensing Buttons
  Integrated Temperature Sensor
External System
  On-Chip Internal DC-DC Converter
  Very Few External Components
  Seamless Integration With the SimpleLink CC1190 Range Extender
Low Power
  Wide Supply Voltage Range: 1.8 to 3.8 V
  Active-Mode RX: 5.5 mA
  Active-Mode TX at +10 dBm: 12.9 mA
  Active-Mode MCU 48 MHz Running Coremark: 2.5 mA (51 µA/MHz)
  Active-Mode MCU: 48.5 CoreMark/mA
  Active-Mode Sensor Controller at 24 MHz: 0.4 mA + 8.2 µA/MHz
  Sensor Controller, One Wake Up Every Second Performing One 12-Bit ADC Sampling: 0.85 µA
  Standby: 0.6 µA (RTC Running and RAM and CPU Retention)
  Shutdown: 185 nA (Wakeup on External Events)
RF Section
  Excellent Receiver Sensitivity –124 dBm Using Long-Range Mode, –110 dBm at 50 kbps
  Excellent Selectivity: 52 dB
  Excellent Blocking Performance: 90 dB
  Programmable Output Power up to +14 dBm
  Single-Ended or Differential RF Interface
  Suitable for Systems Targeting Compliance With Worldwide Radio Frequency Regulations
    ETSI EN 300 220, EN 303 131, EN 303 204 (Europe)
    FCC CFR47 Part 15 (US)
    ARIB STD-T108 (Japan)
  Wireless M-Bus and IEEE 802.15.4g PHY
Tools and Development Environment
  Full-Feature and Low-Cost Development Kits
  Multiple Reference Designs for Different RF Configurations
  Packet Sniffer PC Software
  Sensor Controller Studio
  SmartRF™ Studio
  SmartRF Flash Programmer 2
  IAR Embedded Workbench® for ARM
  Code Composer Studio™

## Slide 4
Hardware: Sensor
Light Sensor
LM393 | BH 1750
Using photoresistor Split−Supply Range: ±1.0 Vdc to ±18 Vdc Output 0-1023 value analog and digital Data protocols: Analog and digital http://hshop.vn/products/cam-bien-anh-sang-quang-tro-2 35.000 VND | Using photodiode Split−Supply Range:3.3 ­> 6v DC Output 16bit digital Data protocols: I2C http://hshop.vn/products/cam-bien-cuong-do-onh-song-lux-bh1750 60.000 VND
Notes: Quang trở = quang diot

## Slide 5
Hardware: Sensor
Temperature and Humility
Sensor | Specification
AM2315 | H: 0-100% ~ 2% T: -20 -80 c c ~ 0.1 c c Data protocols: I2C 450.000 VNĐ
DHT11 | H: 0-80% ~ 5% T: 0 - 50 c c ~ 2 c c Data protocols: 1x digital 30.000 VNĐ
DHT21 | H: 0-100% ~ 3% T: -40 -80 c c ~ 0.5 c c Data protocols: 1x digital 95.000 VNĐ
DHT22 | H: 0-100% ~ 2-5% T: -40 -80 c c ~ 0.5 c c Data protocols: 1x digital/ 0.5Hz 120.000 VNĐ

## Slide 6
Hardware: Sensor
Soil Humility Sensor
LM393
Output: 0-1023 Data protocols: : Analog or Digital http://hshop.vn/products/cam-bien-do-am-dat-2http://hshop.vn/products/cam-bien-do-am-dat-2 35.000 VNĐ

## Slide 7
Hardware: Sensor
pH Sensor
pH KIT with UART | Atlas scientific pH KIT
Power: 3.3 -5 V Data protocols: UART Full range pH reading from .001 to 14.000 Accurate pH readings down to +/- 0.05 Price: 1,050,000 vnd | Power: 3.3 -5 V Data protocols: UART, I2C Full range pH reading from .001 to 14.000 Accurate pH readings down to +/- 0.02 Price: $149.15

## Slide 8
Hardware: Output

## Slide 9
Sub - Controller
Main Controller
Sensor
Component
Sub - Controller
Sensor
Component
Sub - Controller
Sensor
Component
Web Server
Mobile App
Database
RF
RF
RF
Wi-Fi

## Slide 10
RF
RF
RF
Wi-Fi

## Slide 11
UART
I2C
Digital
Digital/Analog

## Slide 12
TaskSheet Phase 1
Name | Task Assign
Phan Thành Sang | Hardware + MCU Control and managing process Report and Document Support team member
Lê Văn Pháp | Document Web server Web API Database design
Huỳnh Hữu Nghị | Document Android Application Implement Component Connection interfaces
Phạm Hoàng Chinh | Diagram Database Design Document Report Meeting Report